RSpec / GLOSSARY v0.1

# 1. gem install
$ gem install rspec

OR
in Gemfile:
source “https://rubygems.org” / gem "rspec"
$ bundle install --path .bundle

# 2. init RSpec
$ rspec –init
# 3. run options
$ bundle exec rspec --format documentation
$ rspec spec(2nd optional parameter is the dir)

## Parameters
-I PATH	Adds PATH
--fail-fast	stop running specs after the first Example fails
-f, --format / FORMATTER	to specify different output formats
-c, --color	Enables color in rspec’s output.

# 4. spec_helper
All the files can be required in
# spec/spec_helper.rb
# 5. folders
All the test should be in /spec folder
and end with _spec.rb
# 6. require
# spec/caesar_cypher_spec.rb / require "caesar_cypher" / describe CaesarCypher do

# Syntax
### describe
The describe block is always used at the top to put specs in a context. It can accept either a class name, in which case the class needs to exist, or any string you'd like.
class methods are prefixed with a dot (".add")
instance methods with a dash ("#add")

### context
context is technically the same as describe, but is used in different places, to aid reading
### it
to describe a specific example
it is RSpec's way to say "test case"
Generally, every example should be descriptive
### expect
to define expected outcomes
#### one-liner
describe Run.new(40,20,blabla) / it {is_expected.to respond_to(:duration)}
it "responds to '#duration'" do / expect(subject).to respond_to(:duration) / end

RSpec’s subject feature reduces the amount of code. It is convenient when you can avoid duplication between a matcher and the string that documents the test example by moving the object instantiation into the describe line.
## matchers
expect(actual).to eq(expected)
Equality/Identity
eq	eql		be			equal
Comparison
be >	be >=		be <			be <=
be_between			inclusive/exclusive
expect(actual).to be_between(min,max).inclusive
expect(actual).to match(/regex/)
Class/Type
be_instance_of(class)				be_kind_of
respond_to(method)			(instance/class)
Booleans
be true			be false
be_truthy		be_nil			be_falsey
Errors
raise_error(ErrorClass)
raise_error("error message")
raise_error(ErrorClass,"error message")
receive
expect(output).to receive(:puts).with("uo!")

### as_null_object
to ignore any messages that aren't explicitly set as stubs or message expectations.
When you don't care about the object's behavior or interaction, and don't want to explicitly stub everything out that's needed. Calling any method with any arguments on a null object will not result in a NoMethodError or ArgumentError.
it "prompts for the first guess" do / output=double("output").as_null_object / game =Game.new(output) / expect(output).to / receive(:puts).with("uoo:") / game.start / end

## hooks
before(:each) do	after(:all) do

remember to use @instance_variables
### let(:what){ }
When the code in a before block is only creating instance variables and assigning them values (which is most of the time), we can use let()
let(:output){double('output').as_null_object} / let(:game) { Game.new(output) }

it takes a symbol representing a method name and a block, which represents the implementation of that method
# Mocks
involves using fake dependent objects or methods in order to write a test
Dummy – a pure placeholder object with no behaviour (it doesn’t respond to any messages). This is used when a method requires an argument but doesn’t interact with it in a specific test	Fake – a replacement object with real behaviour, but taking shortcuts that are helpful for testing purposes (a good example is using an in-memory database for faster testing of database dependent code).
Spy – an object that records all messages it receives (assuming it is allowed to respond to them), allowing the messages it should have received to be asserted at the end of a test.	Mock – an object that is given a specification of the messages that it must receive (or not receive) during the test if the test is to pass.
Stub – an object providing canned responses to specified messages.

## Stubs
Here we provide an object that is given a set of canned responses to the messages it supports. We just want our stub to respond to the message #prod
it "says what noise it makes" do / thingie = double(:thingie, prod: "oi") / subject = Detective.new(thingie) / result = subject.investigate / expect(result).to eq "It went 'oi'" / end

Here, #double is an RSpec helper method that creates an object with certain properties that we specify. We can give it a label (useful for debugging, particularly when multiple test doubles are in use), and a hash of supported messages and responses.
# 8. examples
## Zombies
# spec/lib/zombie_spec.rb
require "spec_helper" / describe "A Zombie" do / it "is named Ash" / end
$ rspec spec/lib/zombie_spec.rb

zombie.propriety.should == 'uoo'/false/>5 / zombie.alive.should be_false / zombie.height.should_not == 5 / tweet.status.length.should be >= 140

## StringCalculator
# spec/string_calculator_spec.rb	Path
describe StringCalculator do / describe ".add" do / context "empty string" do / it "returns zero" do / expect(StringCalculator.add / ("")).to eql(0) / end / end / end / end	File
$ bundle exec rspec	Run

# 9 config
## Color output
add --color to a .rspec file to the project dir root
(or, place the .rspec file in your ~/home dir to have it for all projects)
NYANSPEC install the gem nyan-cat-formatter and put the options in the .rspec file --format NyanCatFormatter

# Cheat Sheet
## The Basics
An example that uses common RSpec features.
RSpec.describe 'an array of animals' do
 let(:animal_array){ [:cat,:dog,:mule] }

  it 'has three animals' do
    expect(animal_array.size).to eq(3)
  end

  context 'mutation' do
    after {expect(animal_array.size).not_to eq(3)}

    it 'can have animals added' do
      animal_array << :cow
      expect(animal_array).to
 eq([:cat, :dog, :mule, :cow])
    end

    it 'can have animals removed' do
      animal_array.pop
      expect(animal_array).to
 eq([:cat, :dog])
    end
  end
end
## Let
Variables that are recreated for every test.
RSpec.describe 'Uses of `let`' do
  let(:random_number) { rand }
  let(:lazy_creation_time) { Time.now }
  let!(:eager_creation_time) { Time.now }

  it 'memoizes values' do
    first = random_number
    second = random_number
    expect(first).to be(second)
  end

  it 'creates the value lazily' do
    start_of_test = Time.now
    expect(lazy_creation_time).to be >
 start_of_test
  end

  it 'creates the value eagerly using
 `let!`' do
    start_of_test = Time.now
    expect(eager_creation_time).to be <
 start_of_test
  end
end
## Subject Under Test
Convenience methods for accessing the subject under test, for more concise tests. Like let, the subject object is recreated for every test.
RSpec.describe Array do
  it 'provides methods based on the
 `RSpec.describe` argument' do
    # described_class = Array
    expect(described_class).to be(Array)
    # subject = described_class.new
    expect(subject).to eq(Array.new)
    # is_expected = expect(subject)
    is_expected.to eq(Array.new)
  end

 context 'explicitly defined subject' do
    # subject can be manually defined
    subject { [1,2,3] }
    it 'is not empty' do
      is_expected.not_to be_empty
    end
  end

  context 'can be named' do
  #you can provide a name, just like `let`
    subject(:bananas) { [4,5,6] }
    it 'can be called by name' do
     expect(bananas.first).to eq(4)
    end
  end
end
## Hooks
Run arbitrary code before or after each test or context.
RSpec.describe 'Hooks' do
  order = []

 before(:all) { order << 'before(:all)'}
 before { order << 'before' }
 after { order << 'after' }
 after(:all) { order << 'after(:all)';
puts order }

  around do |test|
    order << 'around, pre'
    test.call
    order << 'around, post'
  end

  it 'runs first test' do
    order << 'first test'
  end

  it 'runs second test' do
    order << 'second test'
  end
end
Execution order for the tests above:
1. before(:all)
2. around, pre
3. before
4. first test
5. after
6. around, post
7. around, pre
8. before
9. second test
10. after
11. around, post
12. after(:all)
## Skipping
Temporarily prevent tests from being run.
RSpec.describe 'Ways to skip tests' do
  it 'is skipped because it has no body'

  skip 'uses `skip` instead of `it`' do
  end

  xit 'uses `xit` instead of `it`' do
  end

  it 'has `skip` in the body' do
    skip
  end

  xcontext 'uses `xcontext` to skip a
group of tests' do
    it 'wont run' do; end
    it 'wont run either' do; end
  end
end
## Pending
Temporarily ignore failing tests.
RSpec.describe 'Ways to mark failing
 tests as "pending"' do
  pending 'has a failing expectation' do
    expect(1).to eq(2)
  end

  it 'has `pending` in the body' do
    pending('reason goes here')
    expect(1).to eq(2)
  end

  pending 'tells you if a pending test
 has been fixed' do
 # Pending tests are supposed to fail.
 # This test passes, so RSpec will give
 # an error saying that this pending
 # test has been fixed.
    expect(2).to eq(2)
  end
end
## Alternate Syntax
RSpec has aliases for describe and it.
They function exactly the same, but the different wording might be clearer reading the tests.
These are the default aliases:
- Groups: context, example_group, describe
- Examples: it, example, specify
RSpec.describe 'Alternate syntax' do
  example_group 'alernative to
 "context"' do
    example 'alternative to "it"' do
      expect(2).to eq(2)
    end
  end

  describe 'alternative to "context"' do
    specify 'alternative to "it"' do
      expect(2).to eq(2)
    end
  end
end
## Defining Methods
Define arbitrary methods for use within your tests.
RSpec.describe 'Defining methods' do
 def my_helper_method(name)
  "Hello #{name}, you just got helped!"
  end

  it 'uses my_helper_method' do
    message = my_helper_method('Susan')
    expect(message).to eq('Hello Susan,
 you just got helped!')
  end

 context 'within a context group' do
  it 'can still use my_helper_method' do
      message = my_helper_method('Tom')
      expect(message).to eq('Hello Tom,
you just got helped!')
    end
  end
end
## Shared Examples
A reusable set of tests that can be included into other tests.
RSpec.shared_examples 'acts like non-nil
 array' do
  it 'has a size' do
    expect(subject.size).to be > 0
  end

  it 'has has non-nil values for each index' do
   subject.size.times do |index|
    expect(subject[index]).not_to be_nil
   end
  end
end

RSpec.describe 'A real array' do
  include_examples 'acts like non-nil array' do
    subject { ['zero', 'one', 'two'] }
  end
end

RSpec.describe 'A hash with integer keys' do
  include_examples 'acts like non-nil array' do
    subject { Hash[0 => 'zero', 1 =>
 'one', 2 => 'two'] }
  end
end
## Shared Context
A reusable context setup (hooks, methods, and lets) that can be included into other tests.
RSpec.shared_context 'test timing' do
  around do |test|
    start_time = Time.now
    test.call
    end_time = Time.now
    puts "Test ran in #{end_time -
 start_time} seconds"
  end
end

RSpec.describe 'big array' do
  include_context 'test timing'

  it 'has lots of elements' do
    big_array = (1..1_000_000).to_a
    expect(big_array.size).to eq(1_000_000)
  end
end

# cucumber
Feature: code-breaker starts game / As a code-breaker / I want to start a game / So that I can break the code / Scenario: start game / Given I am not yet playing / When I start a new game / Then I should see "Welcome to CB!" / And I should see "Enter guess:"

Scenario is followed by a string and then a series of steps. Each step begins with any of five keywords: Given, When, Then, And, and But.
Given represents the state of the world before an event	When / represents the event
And and But take on the quality of the previous step	Then represents the expected outcomes

## language selection
Cucumber determines the language based on the types of files in	features/step_definitions
or	features/support
## files and folders
super-basic structure:
root / ├── features / │ ├── codebreaker_starts_game.feature / │ ├── cdbrker_submits_guess.feature / │ ├── step_definitions / │ │ └── codebreaker_steps.rb / │ └── support / │ └── env.rb / └── lib / ├── codebreaker / │ └── game.rb / └── codebreaker.rb

## Scenario Outline
features/cdbrkr_submits_guess.feature
Feature: code-breaker submits guess / Scenario Outline: submit guess / Given the secret code is "<code>" / When I guess "<guess>" / Then the mark should be "<mark>" / Scenarios: no matches / | code | guess | mark | / | 1234 | 5555 | |

features/step_definitions/cbrkr_steps.rb
Given /^I am not yet playing$/ do / end / When /^I start a new game$/ do / Codebreaker::Game.new.start / end

## Given
when Cucumber sees the
Given I am not yet playing

step in the scenario, it strips off the Given and looks for a Regexp that matches the string
I am not yet playing .

At this point, we have only one step definition, and its Regexp is /^I am not yet playing$/ , so Cucumber executes the associated block from the step definition.
Since there is nothing in the block yet, there is nothing that can go wrong, so the step is considered passing
## When
The When is where the action is.